## Slide 1: A realistic simulation of the AGATA Demonstrator +PRISMA Spectrometer
Elif INCE, Istanbul University
7 th AGATA Week, 08-11 July 2008

## Slide 2: Outline
The Agata Demonstrator+ Prisma Spectrometer
Aim of this work: “ Realistic” event generation of AGATA+ PRISMA coupling
Preliminary results
Work in Progress...

## Slide 3: The AGATA Demonstrator Objective of the final R&D phase 2003-2008
Main issue is Doppler correction capability coupling to beam and recoil tracking devices
<1 symmetric triple-cluster>
5 asymmetric triple-clusters
15 36-fold segmented crystals
540 segments
555 digital-channels
Eff. 3 – 6 % @ M = 1
Eff. 2 – 4 % @ M = 30
Full ACQ with online PSA and
-ray tracking

## Slide 4
MCP
Position at the entrance
x,y-->(,)
time --> T
(Start for TOF)
PRISMA Spectrometer
Quadrupole focuses
the ions vertically
towards the dispersion
plane
Dipole magnet bends
ions horizontally according to their
magnetic rigidity (Bρ)
MW-PPAC
(Focal plane detector )
position--> X,Y
time --> T
(Stop for TOF)
Ionization Chamber (IC)
∆E--> Energy loss
E --> Total energy

## Slide 5
to produce realistic event generator
for multi-nucleon transfer reactions
and direct reactions.
to evaluate the performance of the AGATA+PRISMA setup in a consistent way.
Aim of this work
Notes: <number>

## Slide 6: How to proceed?
1. “schematic” event generation (completed!)
2. “Replay" real data into the simulation (work in progress)
3. Develop a full code to calculate cross-sections and angular distributions.

## Slide 7: “Schematic” event generation for AGATA+ PRISMA
Realistic events were created and used as an input for AGATA+PRISMA simulation according to results from a performed CLARA-PRISMA experiment.
90Zr + 208Pb (0.300mg/cm², @ 45.0°)
projectile energy:560 MeV
Projectile-like energy:346.2 MeV(average energy)
(29% FWHM dispersion)
1 -ray (1000keV) from each ion in order to see Doppler correction effects of AGATA Demonstrator.
Notes: <number>

## Slide 8: Simulation of the Agata Demonstrator+Prisma Coupling
Conditions set:
Demonstrator Geometry (5 triple clusters)
Demonstrator distance: 14 cm to target.
Number of Events: 100.000
2.Mgt (Mars Gamma Tracking): used for producing
tracked gammas. (D.BAZZACCO)
3.CMerge (Clara+Agata Merge): used for combining
“Agata+Prisma” into a single data file.(E.FARNEA)

## Slide 9: Effect of the recoil velocity

## Slide 10: Doppler correction capabilities

## Slide 11
Assuming that 3 projectile-like ions were obtained from the reaction emitting photons with very close energies;
90Zr (1000 keV)
91Zr (1003 keV)
89Y (998 keV)
90Zr + 208Pb (0.300mg/cm², @ 45.0°)
projectile energy:560 MeV
projectile like energies:(29% FWHM dispersion)
90Zr--> 346.2 MeV
91Zr--> 344.7 MeV
89Y--> 343.8 MeV
“Schematic” event generation for more complicated step using 3 projectile-like
Notes: <number>

## Slide 13: Projections of Ions

## Slide 15
Assuming that 4 projectile-like ions were obtained from the reaction emitting photons with very close energies;
90Zr (1000 keV)
91Zr (1003 keV)
89Y (998 keV)
90Y (999 keV)
90Zr + 208Pb (0.300mg/cm², @ 45.0°)
projectile energy:560 MeV
Projectile-like energies:(29% FWHM dispersion)
90Zr--> 346.2 MeV
91Zr--> 344.7 MeV
89Y--> 343.8 MeV
90Y--> 341.8 MeV
“Schematic” event generation for more complicated step using 4 projectile-like
Notes: <number>

## Slide 17: Projections of Ions

## Slide 19: Work in Progress..
The idea is to obtain a realistic ion distribution by "replaying" real data into simulation.
48Ca+238U(@310MeV) reaction was considered.
(CLARA-PRISMA experiment, Daniele Mengoni, Jose Javier Valiente-Dobon)
Mass spectra were produced of PRISMA standalone-simulation.

## Slide 20: Produced masses from Simulated Data

## Slide 21
Comparison of “Ca” ion’s for Simulated&Real data