## Slide 1: Front End Processing Working Group
Digitisation P.Medina
Pre-processing I.Lazarus
GTS M.Bellato
PSA P.Desesquelle R.Gernhäuser
7th AGATA Week, Uppsala, July 8-11, 2008

## Slide 2: Structure of EDAQ
Detector
preamps
Digitisers
Tracking
Control,
Storage…
Event Builder
Pre-processing
PSA
Core +
36 seg.
Gobal Trigger
Clock
100 MHz
T-Stamp
Ancillary
Ancillary
Ancillary
interface to GTS via mezzanine
merge time-stamped data into event builder
prompt local trigger available from digitisers
Ancillary
detectors
Global Level
Detector
Level

## Slide 3: Initial Data rates for Demonstrator 15 detectors, 10 kHz singles, GL-trigger, Ancillary  1 kHz into PSA
200 B/ev
0.2 MB/s
200 MB/s
36+2  8 kB/event
~8 MB/s
0.2 MB/s
100 Ms/s
14 bits
Pulse
Shape
Analysis
AGATA
Merge
-ray tracking
HL-Trigger, Storage
On Line Analysis, …
SEGMENT
GLOBAL
Energy + · · ·
15*0.2  3 MB/s
save ~100 samples
of signal rise time
E, t, x, y, z,...
DETECTOR
LL-Trigger (CC)
ADC
Pre-processing
+
-
GL-Trigger
1 ms/event
Ancillary
Merge
Initially traces will be recorded for off-line validation
(+ 120 MB/s written out at PSA level)

## Slide 4: General schedule for 2008
Q1
  Reworked ATCA Carrier
  Reworked Segment Mezzanines
  New Core Mezzanine
Q2
  Electronics for one detector; VHDL revision -1
  Start series production of all modules
    36+ ATCA carriers IPN Orsay
    108+ Segment Mezz. 18+ Core Mezz. CSNSM Orsay
    30+ GTS mezzanines INFN Padova
Q3
  Electronics for one triple cluster; VHDL revision 0
Q4
  Phased delivery of final electronics
Slide from the previous AGATA week (Nov. 2007 @ LNL)
MUST BE UPDATED

## Slide 5: Program of session 7
Digitizers  Patrice M. / Patrick C.S.
Pre-processing electronics  Ian L.
  ATCA Carriers and TCKL board
  Processing mezzanines
  Readout to PSA
GTS and global trigger 
Integration of electronics  Dino B.