## Slide 1
Concept of the scanning table in Strasbourg
François DIDIERJEAN
Tatjana FAUL, Fabrice STEHLIN
Strasbourg
AGATA week. 8 - 11 July 2008
Uppsala, Sweden

## Slide 2
X-Y scanning table of Strasbourg
detector  fixed position
radioactive source and collimator  X - Y moving
to improve the device to access to the Z information

## Slide 3
Scheme of the scanning table of Liverpool
BGO
Pb collimator
slites 1.5 mm
Z

## Slide 4
Position sensitive
scintillator detector
Objectives : 1. use a unique position sensitive detector
2. increase the number of slites
662 keV
288 keV
to find the minimal distance between 2 slites to disentangle 2 diffused 

## Slide 5
electronics
GSO scintillator
5 cm x 5 cm x 2 mm
PM, Hamamatsu
8 x 8 pixels
Pb collimator
241Am
Validation tests of the concept
the experimental setup :

## Slide 6
Validation test of the GSO-PM block
241Am
Real position (mm)
Measured position (mm)
linear variation except for the last 5 mm  saturation due to the border effect

## Slide 7
241Am
Variation of the slite-to-slite distance
2, 3, 4, 5, 6 mm

## Slide 8
Variation of the slite-to-slite distance
Measured position (mm)
3 mm / 21 % overlapp
4 mm / 12 % overlapp
5 mm / 4 % overlapp

## Slide 9
Proposed scheme of the Strasbourg scanning table
(collimator thickness 4 mm, slites 1.5 mm)
16 slites 1.5 mm

## Slide 10
GEANT 4 simulations
scintillators
1 cm x 5 cm x 3 mm
BGO or LaBr3 or LSO
10000  -rays of 288 keV
to determine the best scintillator detector type
to see the effect of the scattering

## Slide 11
BGO scintillator (1cm)
8195
764
171
174

## Slide 12
GSO scintillator (1cm)
7214
1233
253
297

## Slide 13
LaBr3 scintillator (1cm)
2912
2499
330
282

## Slide 14
LaBr3 scintillator (2 cm)
4378
3396
645
632

## Slide 15
Conclusions.
The Choice of the scintillator should be BGO which presents the smaller spot size composed of Compton scattering interaction points.
To do list :
Geant simulation calculations to determine the optimal dimension of the scintillator (in particular the thickness).
validation test with radioactive source (288 keV  rays) to decide the use of
* a large scintillator coupled to segmented PM.
* a set of thin scintillators coupled each one to a PM via optical fibers.