## Slide 1: In-beam performance of AGATA-DEMONSTRATOR
Ideas for the firsts commissioning experiments of the AGATA-DEMONSTRATOR campaign at LNL-Legnaro
F. Recchia INFN-LNL

## Slide 2: The “standard” experiment


Position resolution
Angular resolution
Energy resolution
“Standard” experiment: Doppler correction capabilities exploited to measure the position sensitivity

## Slide 3: The main requirements
Simplicity of setup
Simplicity of analysis
Short beam-time request: easy to recover in case of problem with the setup
Flexible solutions for the beam requested
If possible: improved position resolution determination
Our proposal should fulfill all this!!

## Slide 4: Past experience
2002 – MARS experiment:
  Coulex reaction,
  Silicon detector in coincidence
2005 – In-beam experiment of a symmetric prototype detector:
  Fusion evaporation
  No ancillaries
2005 – First AGATA experiment, triple cluster:
  Many reaction channels
  DSSSD detector in coincidence
GRETA experiments: no ancillaries

## Slide 5: Triple-cluster experiment
Full statistics used
PSA algorithm: Grid Search
32 keV
11 keV
4.8 keV
(d,p) reaction through fusion-evaporation
~5 mm

## Slide 6: “Weak points” of past measurement
Grid Search
Recursive Subtraction
Matrix Method
Miniball Algorithm
Result of simulation, few possibilities of cross-check on input parameters
All segment folds Full statistics
beam spot
quality of detector a posteriori positioning
angular and beta dispersion of the beam
One year of pre-sort: not available for the commissioning experiments!!
The input parameters of simulation are not all well determined – they are the main source of errors of the final result

## Slide 7: New strategy (I)
Do not use ancillary detectors
  Data analysis will be concentrated only on gamma part!
  Channel identification using only gamma
Large cross section
  Fusion-evaporation reaction
Minimum spread in direction is required as average direction Doppler correction will be used
  Selection of channels with only neutrons evaporation (without Coulomb barrier)
Close enough to the target: the position uncertainty will dominate the peak broadening in the gamma-spectrum

## Slide 8: New strategy (II)
beam
dcloser
dfarther
beam
Comparison of the experimental result to simulation
Comparison of the experimental results with the detectors at 2 different distances from the target

## Slide 9: The estimation method for position resolution
The only difference between the 2 positions is in the position uncertainty (once the count rate is adjusted)
p (the position resolution) can be estimated
Inverting the error on the estimation of the position resolution it is possible to express a F.O.M. to choose the reaction:
a2 = counting rate contribution

## Slide 10: Reactions
Many possibilities with LNL available beams:
  82Se (220 MeV) + 9Be→ 88Sr (350 mb)
  86Sr (250 MeV) + 9Be→ 92Mo (200 mb)
  104Pd (350 MeV) + 9Be→ 110Sn (160 mb)
  106Pd (350 MeV) + 9Be→ 112Sn (210 mb)
  85Rb (240 MeV) + 7Li→ 90Zr (90 mb)
  84Kr (300 MeV) + 9Be→ 90Zr (600mb)
  82Se (385 MeV) + 12C→ 90Zr (700mb)
  107Ag@ 360 MeV + 7Li → 112Sn (120 mb)
  104Ru@ 450 MeV + 12C → 112Sn (300 mb)
  134Xe@ 600 MeV + 12C → 142Nd (390 mb)
  135Ba@ 560 MeV + 12C → 144Sm (180 mb)
  Good candidates with 2H and H targets if available
Good cross sections!
PACE calculations

## Slide 11: Reactions
Schematic parametric calculation: Monte Carlo simulation not performed
Region of interest
PACE calculations

## Slide 12: TANDEM beam
Different distances between the target and the detectors: 3,7,10,14 cm
Below the Coulonb barrier for all possible contaminants

## Slide 13: TANDEM + ALPI beam
12C is a very simple target, as thin as we want
  134Xe beam 600 MeV 12C target → 142Nd (390 mb)
  2+0+ 641keV
  Distances
  3cm
  7cm
  10cm
  14cm

## Slide 14: PIAVE+ALPI beam
12C is a very simple target, as thin as we want

## Slide 15: F.O.M. comparsion
ROI
Best measurement conditions

## Slide 16: Beam time
Triple cluster experiment performed in Cologne:
  rate was 40 Hz (DAQ slow)
  ~7 days of real beam time (= 170 h)
Acquiring at 2 KHz/crystal we need only 3-4 h to obtain the same statistics (and having only one triple cluster!)
Beam time request depends on the time needed for setup the measurement, not on the run time

## Slide 17: Conclusions
Simplicity of setup
Simplicity of analysis
Short beam-time request: easy to recover in case of problem with the setup
Flexible solutions for the beam requested
If possible: improvement of estimation of position resolution
No ancillaries
3-4 h to collect the same statistics of the triple-cluster experiment
Many different solutions investigated and to be chosen on the basis of accelerators status
Large improvement in precision, less dependency on Monte-Carlo simulations, if just the same statistics available
THANK YOU
All the requirements are met
Monte-Carlo simulations in next talk by Pär-Anders Söderström