## Slide 1
Gamma Tracking
clustering : deterministic annealing filter (DAF)
Last results
AGATA week. 8 - 11 July 2008
Uppsala, Sweden
François DIDIERJEAN
Strasbourg

## Slide 2
clustering method :
deterministic annealing filter (DAF)
Reminder
global distortion :
goal : to minimize the global distortion with the smaller number of clusters.
By analogy with the statistical physics : introduce a Lagrange multiplier. Then, the free energy : F = D - TS
The DAF method corresponds to minimize the Lagrangien F while lowering the system temperature.
As the temperature is lowered, the system undergoes a sequence of phase transitions which consists of a natural split of the cluster in two parts (conducting to an increase of the cluster number).

## Slide 3
The process stops when the system temperature, T, is smaller than Tmin. This stopping temperature is empirically determined and depends on the number of the data interaction points.
E = 1 MeV
Multiplicity : M5
Tmin = 1
Tmin = 0.1
Tmin = 0.01

## Slide 4
Search of the empirical stopping temperature :
Variation of the efficiency (b) and the peak-to-total ratio (c) as a function of the stopping temperature for different -ray multiplicities
(a) Distribution of the number of interactions as a function of 1MeV -ray multiplicity.
Tmin is chosen in respect of the physics
deep inelastic
fusion-evaporation reaction
: high multiplicity
Fragmentation
transfer reaction
Coulomb excitation
: low multiplicity

## Slide 5
Spectra of 1MeV  rays :
Original spectrum obtained from the GEANT4 simulation (a).
Reconstructed spectra using the deterministic annealing filter and the forward tracking algorithm for different -ray multiplicities :
(b) M = 1
(c) M = 2
(d) M = 30

## Slide 6
E multiplicity  (%) P/T (%)
Efficiency and peak-to-total ratio values calculated using the deterministic annealing filter clustering and the forward tracking algorithm for different -ray energies and different multiplicities.
The values in brackets are obtained using the "cones" clustering method.

## Slide 7
Simulated spectra of a rotational band of 30  rays in the 80 keV to 2690 keV energy region in steps of 90 keV.
Original spectrum obtained from the GEANT4 simulation (a) and reconstructed spectra (b).

## Slide 8
future prospects :
1. Comparison between the DAF and the "cone" methods for a set of energies and gamma multiplicities.
4. Application of the DAF method to the probabilistic tracking.
2. Test of the method with real data taken from the AGATA demonstrator.
3. Adaptation of the probabilistic tracking method to the spherical geometry of AGATA.