## Slide 1: On the origin of Differential Crosstalk in segmented detectors
B. Bruyneel for the AGATA week , Uppsala, Sweden July 2008

## Slide 2: Cross talk analysis: Motivation
Crosstalk is present in any segmented detector
Influences energy: Creates strong energy shifts proportional to fold
Influences PSA: Crosstalk mixes with transient signals
Fast and accurate crosstalk detection and energy correction methods developed
To Do : Crosstalk measurement and correction in PSA
Sum of segment Energies vs fold
Xtalk signal:
Notes: For the last part of my talk, I would like to draw the attention to a problem common to any segmented detector : namely cross talk.
This creates strong energy shifts in the segment sum energy, and this proportional to the hit multiplicity:
Doubles are shifted compared to singles. Three folds even more, and so on. >>
If one analyzes the doubles, one observes that it does not simply consists of a single peak, but:
By sorting the two folds into all possible twofold combinations, one observes that the centroids of these peaks are individually shifting according to a regular patten.
The same happens in the core,however there is no such offset observed as is in the segments.
There is thus real physics behind this phenomenon.
>>

## Slide 3: Crosstalk in all its forms
PA
V0,out
V1,out
PA
Zin
Z01
Xtalk ~ Zin / Z01
Proportional Xtalk model : Zin = Miller = 1/sACfb
But: Miller does not explain risetime of preamplifier…!
Proportional Xtalk (50s decay)  Energy
Differential Xtalk (only during risetime)  PSA
Pure Xtalk signal:

## Slide 4: Preamp model describing risetime
Vout/Iin = Zfb
Zin = Vin/Iin
Zin = Zfb/A + Rcold
“Cold Resistor” : - E. Gatti and P. Manfredi – Il Nuovo Cimento vol. 9 serie 3 (1986)
- “Analogue circuits techniques Part II ” F. Anghinolfi , CERN (2002) – (available online)
PA
Vout
Vin
Iin

## Slide 5: Xtalk extension
PA
V0,out
V1,out
PA
Zin
Z01
With Zin = 1/sACfb + Rcold
Xtalk ~ Zin / Z01 = C01/ACfb + s . Rcold C01
Proportional + Differential Xtalk
Example : Rcold = 1k; C01 = 10pF
Differential Xtalk = 1000%ns
Warning: Other ways possible to create Derivative Xtalk !

## Slide 6: Realistic simulation (Multisim)
PA
V0,out
V1,out
PA
10pF
Realistic Preamp model
V0,out
V1,out

## Slide 7: Differential Xtalk from Proportional Xtalk?
A2..A6
B1
F1
Core to seg capacity
Segment labeling:
Sectors: A...F
Rings: 1...6
X
Seg to seg
capacities?
Differential Xtalk will show up in adjacent segments and within same sector

## Slide 8: How to measure …?
B. Bruyneel et al. NIM A 569 (2006) 774-789 / MGS workshop (April 2005) / AGATA week (Nov 2005)

## Slide 9: How to measure…?
(2) “Pulse Shape Characterization and Simulation
for the TIGRESS Gamma-ray Detector “
Thesis Robin Prest TRIUMF 2005
http://www.physics.uoguelph.ca/Nucweb/tigress.htm
“Differential Analysis” using mirror interaction points:
“differences from transients of mirror interactions are pure”
5
6
8
7
(a,b)
•(b,a)
Differential analysis.
for simulation (green)
and experiment (red)
Simulated signal (green) compared
to experimental signal (red)
suffering from cross-talk