## Slide 1: AGAVA INTERACE
Barbara Dulny

## Slide 2: Overview
Tests in VXI system at Ganil
Tests in CBLT mode at Legnaro
Test of new release of AGAVA with the new release of GTS mezzanine card
Plans

## Slide 3: Tests in VXI system at Ganil
Tests of AGAVA in VXI environment done in October 2007 with Frederic Saillant and Co.
Tests were not finished because of time limitation and have to be continued
It was agreed to continue the tests with the new version of AGAVA
The new AGAVA is ready for the tests since May 2008

## Slide 4: Tests in CBLT mode at Legnaro
The test of CBLT mode was done in Legnaro on 5- 9 May 2008 with Sergio Brambilla
Test was done using
  Struck PCI/cPCI to VME interface,
  AGAVA board release 1 and 2,
  CAEN V775 32 channel TDC,
  CAEN V785 32 channel ADC
  CAEN V538A 8channel NIM-ECL/ECL-NIM Translator
AGAVA was the first, TDC intermediate, ADC last in the chain
External trigger (~20kHz pulser) was used for AGAVA input
KMAX software was used on the Struck for control and data collection
Test was running whole night (>8 hours) with total acqusition rate ~10 kHz

## Slide 5: Tests of new release of AGAVA
The AGAVA rel. 2 was tested in the same configuration as rel.1 in the CBLT mode and standard VME access mode successfuly
As the GTS release 1 (based on Virtex 2Pro) will be not produced anymore it was necessary to test AGAVA board with the new GTS release 2 (based on Virtex 4)
The tests of AGAVA release 1 and 2 with new GTS (release2) have been done in CBLT and standard mode successfully
The test of the Ethernet connection to the GTS via AGAVA release 2 was not successful because there were still missing components on the AGAVA release 2 (promissed from GTS team)
The Ethernet connection test should be tested.

## Slide 6: Next
Continue tests in the VXI environment at Ganil
Test of Ethernet connection to the GTS via AGAVA board release 2.