## Slide 1
Precision Spectroscopy of Exotic Nuclei using AGATA
AGATA
Mike Bentley & UK AGATA Collaboration
What is AGATA?
Recent physics highlights from AGATA
AGATA technology in the UK

## Slide 2
Precision spectroscopy of nuclear states
Gamma-ray (hence level) energies
Complex level schemes (γn coincidences)
(high resolution essential – i.e. Ge)
Precision probes of the nuclear wave function:
Lifetimes (transition matrix elements)
Electromagnetic moments
Cross-sections for direct reactions
Gamma-ray spectroscopy

## Slide 3
Low intensity
High background
Large Doppler broadening
High counting rates
High gamma-ray multiplicities
FAIR (Germany)
SPIRAL (France)
SPES (Italy)
HIE-ISOLDE (CERN)
The need for AGATA
The challenge of the new generation of radioactive beam facilities
The ideal γ-ray spectrometer
High efficiency
Distinguish gammas from b/g
Highly position sensitive
High data throughput
Can distinguish multiple gammas
v/c ~ 50%
Radioactive beam of 46Cr
AGATA (GSI)
2+ -> 0+

## Slide 4
180 hexagonal crystals: 3 shapes
3 fold clusters (cold FET): 60 all equal
Inner radius (Ge): 23.5 cm
Amount of germanium: 362 kg
36-fold segmentation 6480 segments
AGATA Definition: NIM A 668 (2012) 26
What is AGATA?
13 Countries, >40 Institutions
Solid Sphere of Ge material: Solid angle coverage ~ 82 %
36-fold segmentation of crystal
Track each gamma interaction through the crystal
Reconstruct and disentangle gammas

## Slide 5
The concept of γ-ray tracking
Highly segmented
HPGe detectors
Identified
interaction points
(x,y,z,E,t)i
Evaluation of permutations of interaction points
Digital electronics
to record and process signals
1
2
3
4
Reconstructed g rays
Pulse Shape Analysis to decompose recorded waves
g

## Slide 6: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,10,46)
measured
(10,30,46)
791 keV deposited in segment B4

## Slide 7: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
791 keV deposited in segment B4
(10,10,46)
measured calculated

## Slide 8
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,15,46)
791 keV deposited in segment B4
measured calculated
Pulse Shape Analysis concept

## Slide 9: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,20,46)
791 keV deposited in segment B4
measured calculated

## Slide 10: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,25,46)
791 keV deposited in segment B4
measured calculated

## Slide 11: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,30,46)
791 keV deposited in segment B4
measured calculated

## Slide 12: Pulse Shape Analysis concept
Result of Grid Search algorithm
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,25,46)
791 keV deposited in segment B4
measured calculated

## Slide 13
2012-2014
GSI, Germany
~25 detectors
AGATA at GSI
2014-2021
GANIL, France
45 -> detectors
AGATA at GANIL
2021-2024
Legnaro, Italy
60 -> detectors
AGATA at LNL
2025 ->
FAIR, Germany
80-90 detectors
AGATA at NUSTAR
The AGATA journey…
Reaccelerated RIBs:
Coulomb Excitation, Direct Reactions, MNT, Deep Inelastic, Fusion
Direct and inverse kinematics b ~ 10%
In-flight RIBs:
Relativistic Coulomb Excitation, Knockout, Fragmentation.
b ~ 50%

## Slide 14
Recent Highlights at GANIL
2014-2021
GANIL, France
45 -> detectors
AGATA at GANIL

## Slide 15
Neutron-proton pairing in N = Z nuclei
Search for np T=0 pairing in N=Z nuclei, evidence is elusive
Is there a “fluid” of T=0 np pairs along with “normal” T=1 pairs?
T=0 pairing may respond differently to rotational motion
Look for delayed rotational alignments in heavy N=Z nuclei
S. Frauendorf, A.O. Macchiavelli, Prog. in Particle and Nuclear Physics 78, 24 (2014)
ISOVECTOR
ISOSCALAR
Moment of inertia = I / ω ()

## Slide 16
Fusion Reaction: 36Ar + 54Fe  88Ru + 2n + γ
Cross section σ ~ few μb
N=Z 88Ru studied using AGATA
Bo Cederwall, KTH Stockholm
Bob Wadsworth, University of York
et al.
B. Cederwall et al., Phys. Rev. Lett. 124, 062501 (2020)
NEDA (neutron detectors)
Select two-neutron events
DIAMANT (CsI)
Reject charged-particle events
AGATA
Record multiple gamma rays
Power of AGATA:
High Efficiency
Multiple simultaneous γ rays

## Slide 17
New
Delayed alignment (πg9/2)2
…in N=Z system
Summed two-neutron γ-γ spectrum
AGATA
Moment of inertia = I / ω ()
Bo Cederwall, KTH Stockholm
B. Cederwall et al., Phys. Rev. Lett. 124, 062501 (2020)
N=Z 88Ru studied using AGATA

## Slide 18
15O + α studied using AGATA: A crucial reaction in astrophysics
Thermonuclear runaway producing flashes: X-ray bursts
Site of the rp-process creating heavier elements up to A~100
15O captures alpha particle 15O(α,γ)19Ne
Regulates flow between HCNO cycle and rp-process
19Ne 4.033 MeV state biggest contribution to reaction rate
Reaction rate through this state unknown (upper limit)
Neutron stars in binary systems: accrete matter from companion
Hot CNO cycle(s)
= p-capture
= β decay
Jennifer Sanchez Rojo, Christian Diget, University of York

## Slide 19
Power of AGATA:
High Efficiency (4 MeV γ ray)
Position sensitivity (Doppler, v/c 10%)
15O + α studied using AGATA at GANIL
Jennifer Sanchez Rojo, Christian Diget, University of York
15O radioactive beam
Cross section ~ few μb
Very challenging!

## Slide 20
19Ne (VAMOS)-gated Doppler Corrected AGATA Spectrum
15O + α studied using AGATA at GANIL
Jennifer Sanchez Rojo, Christian Diget, University of York
4000
3500
4.033 MeV gamma-ray
Few (10?) counts expected
See Jenn’s talk Tomorrow (Tuesday)
J. Sanchez Rojo
3:45 PM - 4:00 PM Nuclear Astrophysics 1

## Slide 21
48Ca
40Ca
44P
LINE of N=Z
Wilton Catford & Adrien Matta
The single-particle structure of 48K
insights into the important valence interactions
π(s1/2) - ν(f5/2) etc
proton population inversion
48K as a window into shell structure near 44P
48K
Z = 20
Z = 8
N = 28
N = 20
Evolution of shell structure near N = 28

## Slide 22
Wilton Catford & Adrien Matta
d(47K,p)48K at SPIRAL1+ A few weeks ago!
AGATA, MUGAST and VAMOS
106 pps, >99.99% pure radioactive 47K beam
Looking for new excited states in 48K
π(0s1/2)  ν(0f5/2) interaction
Power of AGATA:
High Efficiency (high-energy γ rays, γ-γ analysis)
Position sensitivity (Doppler, v/c 10%)
ONLINE ANALYSIS: Experiment March 2021 (E793s)
VAMOS-gated AGATA spectrum

## Slide 23
GATE Ex(48K) =2.0 MeV
Ex
Eg
Eg
NEWLY IDENTIFIED
STATES &
DECAYS in 48K
Wilton Catford & Adrien Matta
PRELIMINARY ANALYSIS: Experiment March 2021 (E793s)
Thanks to Wilton Catford (Surrey) for the analysis and spectra !
d(47K,p)48K at SPIRAL1+ A few weeks ago!

## Slide 24
UK AGATA Project (STFC): 2020-24
Νext phases of AGATA (SPES and FAIR)
AGATA triple-cluster modules
Detector prototyping and characterisation
Mechanical support structure
Electronics and Firmware
Pulse-Shape Analysis
Simulation
Support structure at LNL
GANIL
γ-interaction heat map

## Slide 25
signal basis generation
Experimental (scanning)
Analytical (calculated)
long acquisition times
experimental conditions change
Physics model, Complex Electric fields
Impurity/n-damage
electronics response
temperature etc
Challenges in pulse-shape analysis
simulated detector response in ADL 3.0

## Slide 26
Group interaction points from different gamma-rays into hit collections
Use Compton formula to order interaction points
Define tracks between interaction points that also link the hit collections with each other
Optimise coordinates of hit collection using the tracks that link their constituent points and Compton formula
PSA Self-calibration (experimental basis set)
Generate an experimental set of position specific waveforms
High-statistics source data
Iterative process using Compton-tracking
S.Heil, S.Paschalis and M.Petri.
Eur. Phys. J. A (2018) 54: 172
Sebastien Heil
Stefanos Paschalis
Marina Petri
University of York

## Slide 27
signal basis generation
Experimental (scanning)
Analytical (calculated)
long acquisition times
experimental conditions change
Physics model, Complex Electric fields
Impurity/n-damage
electronics response
temperature etc
Challenges in pulse-shape analysis
Signal matching (grid search)
Grid Search
University of Liverpool:
Require positions at resolution 5mm
Require positions at resolution ≤ 5mm
Dataset is ~ 50,000 points (37x121)
PSA-grid search needs to be very fast (~ ms)
Experimental validation of Simulation.
Novel PSA techniques for accelerated Grid Search
Machine Learning for Advanced Signal Inference
High resolution simulations of new detectors.
Signal matching (grid search)
University of Liverpool:
Experimental validation of Simulation.
Novel PSA techniques for accelerated Grid Search
Machine Learning for Advanced Signal Inference
High resolution simulations of new detectors.

## Slide 28
Graph-accelerated techniques try to organize data and form efficient searches
Search spaces can be Non-Euclidean, Embedded spaces.
Searching points can be .
Processing rates in region (12-400) kHz.
Machine Learning uses a simulated basis to learn trends via inference e.g. Position Regression, Autoencoding & Fold tagging
No searching is performed whatsoever.
Simulated basis only needed for training.
Needs an appropriate model & good data.
Can be used for hyper-efficient signal compression.
Useful for determining Fold accurately.
FAISS
CNNs
HNSW
KD-Trees
Novel Algorithm Development for PSA
Courtesy of Fraser Holloway, University of Liverpool
F.Holloway@liverpool.ac.uk

## Slide 29
Pencil Beam Reconstruction
Example Optimum Solution for k-NN Method
Novel Algorithm Development for PSA
Courtesy of Fraser Holloway, University of Liverpool
F.Holloway@liverpool.ac.uk
Experimental Results:
See Fraser’s talk Thursday
F. Holloway
12.15 PM Nuclear Structure 4

## Slide 30
Scientific Research Curiosity
Applications
State of the art detectors
Medical
Security
Environment
Societal Impact of AGATA technology
See Laura Harkness Brennan’s talk
Keynote talk
Thursday 10.00

## Slide 31
Conclusions and Thanks
AGATA:
Key device for nuclear physics in Europe
Capabilities enhance future RIB facilities
Huge European technical effort
Thanks:
UKRI-STFC support for AGATA
Staff at GANIL
Slides: Jenn, Wilton, Fraser
AGATA collaboration

## Slide 32
Thank you

## Slide 33
Physics of AGATA
W.Korten et al., Eur. Phys. J A56, 137 (2020)

## Slide 35
Gamma-Ray Energy Tracking Arrays Worldwide
GRETA (USA)
120 Ge crystals
30 Quad “modules”
~17 cm internal diameter
180 Ge crystals
60 Triple “clusters”
~23 cm internal diameter
AGATA (Europe)

## Slide 36
starting condition
after 1st iteration
after 2nd iteration
after 10th iteration
Δr [mm]
Δr [mm]
Δr [mm]
Δr [mm]
RMS = 1.2 mm
R [mm]
PSA Self-calibration (experimental basis set)
University of York:
Demonstrated in simulation only
Needs experimental validation
Detailed analysis underway
S.Heil, S.Paschalis and M.Petri.
Eur. Phys. J. A (2018) 54: 172
Sebastien Heil
Stefanos Paschalis
Marina Petri
University of York